## Slide 1: AHB to APB BRIDGE VERIFICATION
Presentation by Deekshith

## Slide 2: INTODUCTION AND AIM
This project deals with the class based verification of bridge between high speed AMBA AHB(Advanced High Performance bus) and low-power AMBA APB (Advanced Peripheral Bus) in UVM.
The AMBA AHB is for high-performance, high clock frequency system modules.
The AMBA APB is for low-power peripherals.

## Slide 3: FUNCTIONS OF BRIDGE
Latches the address and holds it valid throughout the transfer.
Decodes the address and generates a peripheral select, PSELx.
Only one select signal can be active during a transfer.
Drives the data onto the APB for a write transfer.
Drives the APB data onto the system bus for a read transfer.
Generates a timing strobe, PENABLE, for the transfer.

## Slide 4: BLOCK DIAGRAM OF BRIDGE

## Slide 5: UVM ARCHITECTURE

## Slide 6: AHB DRIVER AND MONITOR LOGIC
AHB driver logic: Wait till Hreadyout is high send control signals along with Haddr in the first clock cycle. In the next clock cycle check if Hreadyout is high and then send Hwdata to DUT.
AHB monitor logic: Wait till Htrans is 2 or 3 and then collect control signals from the interface . In the next clock cycle wait till Hreadyout is high and then collect data signal.Create a copy of collected data and write into the tlm_analysis_fifo using 'write' method.

## Slide 7: APB DRIVER AND MONITOR LOGIC
APB driver logic: Wait till Penable is high and then drive Irdata when Pwrite is low.
APB monitor logic: Wait till Penable is high and check for Pwrite . If Pwrite is high then collect Pwdata and Paddr else collect Hrdata, Paddr and Irdata from the DUT. Send these collected items to second tlm_analysis_fifo in the scoreboard using 'write' method.

## Slide 8: SIMPLE WRITE & READ OPERATION

## Slide 9: TESTCASE DETAILS
Single transfer
4-beat wrapping burst.
4-beat incrementing burst.
8-beat wrapping burst.
8-beat incrementing burst.
16-beat wrapping burst.
16-beat incrementing burst.

## Slide 10: WRAP OPERATION

## Slide 11: COVERAGE REPORT

## Slide 12
THANK YOU